### Interrupt of 8086/8088

### The 8086 series of microprocessors has an Interrupt Vector Table situated at 0000:0000 which extends for 1024 bytes.

### The Interrupt Vector table holds :

| Address | Base | Base+1 | Base+2 | Base+3 |
| --- | --- | --- | --- | --- |
| Content | IP Lower | IP Higher | CS Lower | CS Higher |

### Base = Interrupt No. * 4

### This gives us room for the 256 Interrupt Vectors.

| INT (Hex) | IRQ | Common Uses |
| --- | --- | --- |
| 00 - 01 | Exception Handlers | - |
| 02 | Non-Maskable IRQ | Non-Maskable IRQ (Parity Errors) |
| 03 - 07 | Exception Handlers | - |
| 08-0F | Hardware IRQ0~7 | System Timer, Keyboard, Serial Comms, Sound Card, FD Ctrl, Parallel Comms. |
| 10 - 6F | Software Interrupts | (DOS INT, e.g. 21H) |
| 70 - 77 | Hardware IRQ8~15 | Real Time Clock, Mouse, HD Drive, Co-Processor |
| 78 - FF | Software Interrupts | - |

### Interrupt Sequence

- One or more of the INTERRUPT REQUEST lines (IR7±0) are raised high, setting the corresponding IRR bit(s).

- The 8259A evaluates these requests, and sends an INT to the CPU, if appropriate.

- The CPU acknowledges the INT and responds with an INTA pulse.

- Upon receiving an INTA from the CPU group, the highest priority ISR bit is set and the corresponding IRR bit is reset. The 8259A does not drive the Data Bus during this cycle.

- The 8086 will initiate a second INTA pulse. During this pulse, the 8259A releases an 8-bit pointer onto the Data Bus where it is read by the CPU.

- This completes the interrupt cycle. In the AEOI mode the ISR bit is reset at the end of the second INTA pulse. Otherwise, the ISR bit remains set until an appropriate EOI command is issued at the end of the interrupt subroutine.

### The Initialization Control Words (ICWS)

ICW1 – Interrupt Trigger Type/ Address Interval/ Cascade ?/ With ICW4?

ICW2 – Selects Base Vector Address.

00001000 (0x08) for PIC1 and 01110000 (0x70) for PIC2

ICW3 – Master/ Slave Connection Information.

ICW4 – The only thing we must set is 8086/8080 Mode which is done using Bit 0.

### The Operation Control Words (OCWS)

OCW1 – Interrupt Masks

OCW2 – Selects how the End of Interrupt (EOI) procedure works.

OCW3 – Bits 0 and 1 enable use to read IRR and ISR registers.

| Address | Read/Write | Function |
| --- | --- | --- |
| Base | Write | Initialization Command Word 1 (ICW1) |
|  | Write | Operation Command Word 2 (OCW2) |
|  | Write | Operation Command Word 3 (OCW3) |
|  | Read | Interrupt Request Register (IRR) |
|  | Read | In-Service Register (ISR) |
| Base+1 | Write | Initialization Command Word 2 (ICW2) |
|  | Write | Initialization Command Word 3 (ICW3) |
|  | Write | Initialization Command Word 4 (ICW4) |
|  | Read/Write | Interrupt Mask Register (OCW1) |

### Initialization Command Word 1 (ICW1)

| Bit(s) | Function |
| --- | --- |
| 7:5 | Interrupt Vector Addresses for MCS-80/85 Mode. |
| 4 | Must be set to 1 for ICW1 |
| 3 | 1 | Level Triggered Interrupts |
|  | 0 | Edge Triggered Interrupts |
| 2 | 1 | Call Address Interval of 4 |
|  | 0 | Call Address Interval of 8 |
| 1 | 1 | Single PIC |
|  | 0 | Cascaded PICs |
| 0 | 1 | Will be Sending ICW4 |
|  | 0 | Don't need ICW4 |

### Initialization Command Word 2 (ICW2)

| Bit | 8086/8080 Mode | MCS 80/85 Mode |
| --- | --- | --- |
| 7 | I7 | A15 |
| 6 | I6 | A14 |
| 5 | I5 | A13 |
| 4 | I4 | A12 |
| 3 | I3 | A11 |
| 2 | - | A10 |
| 1 | - | A9 |
| 0 | - | A8 |

### Initialization Command Word 3 (ICW3)

For Master

| Bit | Function |
| --- | --- |
| 7 | IR7 is connected to a Slave |
| 6 | IR6 is connected to a Slave |
| 5 | IR5 is connected to a Slave |
| 4 | IR4 is connected to a Slave |
| 3 | IR3 is connected to a Slave |
| 2 | IR2 is connected to a Slave |
| 1 | IR1 is connected to a Slave |
| 0 | IR0 is connected to a Slave |

For Slave :

| Bit(s) | Function |
| --- | --- |
| 7 | Reserved. Set to 0 |
| 6 | Reserved. Set to 0 |
| 5 | Reserved. Set to 0 |
| 4 | Reserved. Set to 0 |
| 3 | Reserved. Set to 0 |
| 2:0 | Slave ID |
|  | 000 | Slave 0 |
|  | 001 | Slave 1 |
|  | 010 | Slave 2 |
|  | 011 | Slave 3 |
|  | 100 | Slave 4 |
|  | 101 | Slave 5 |
|  | 110 | Slave 6 |
|  | 111 | Slave 7 |

### Initialization Command Word 4 (ICW4)

| Bit(s) | Function |
| --- | --- |
| 7 | Reserved. Set to 0 |
| 6 | Reserved. Set to 0 |
| 5 | Reserved. Set to 0 |
| 4 | 1 | Special Fully Nested Mode |
|  | 0 | Not Special Fully Nested Mode |
| 3:2 | 0x | Non - Buffered Mode |
|  | 10 | Buffered Mode - Slave |
|  | 11 | Buffered Mode - Master |
| 1 | 1 | Auto EOI |
|  | 0 | Normal EOI |
| 0 | 1 | 8086/8080 Mode |
|  | 0 | MCS-80/85 |

### Operation Control Word 1 (OCW1)

| Bit | PIC 2 | PIC 1 |
| --- | --- | --- |
| 7 | Mask IRQ15 | Mask IRQ7 |
| 6 | Mask IRQ14 | Mask IRQ6 |
| 5 | Mask IRQ13 | Mask IRQ5 |
| 4 | Mask IRQ12 | Mask IRQ4 |
| 3 | Mask IRQ11 | Mask IRQ3 |
| 2 | Mask IRQ10 | Mask IRQ2 |
| 1 | Mask IRQ9 | Mask IRQ1 |
| 0 | Mask IRQ8 | Mask IRQ0 |

### Operation Control Word 2 (OCW2)

| Bit(s) | Function |
| --- | --- |
| 7:5 | 000 | Rotate in Auto EOI Mode (Clear) |
|  | 001 | Non Specific EOI |
|  | 010 | Reserved |
|  | 011 | Specific EOI |
|  | 100 | Rotate in Auto EOI Mode (Set) |
|  | 101 | Rotate on Non-Specific EOI |
|  | 110 | Set Priority Command (Use Bits 2:0) |
|  | 111 | Rotate on Specific EOI (Use Bits 2:0) |
| 4 | Must be set to 0 |
| 3 | Must be set to 0 |
| 2:0 | 000 | Act on IRQ 0 or 8 |
|  | 001 | Act on IRQ 1 or 9 |
|  | 010 | Act on IRQ 2 or 10 |
|  | 011 | Act on IRQ 3 or 11 |
|  | 100 | Act on IRQ 4 or 12 |
|  | 101 | Act on IRQ 5 or 13 |
|  | 110 | Act on IRQ 6 or 14 |
|  | 111 | Act on IRQ 7 or 15 |

### Operation Control Word 3 (OCW3)

| Bit(s) | Function |
| --- | --- |
| 7 | Must be set to 0 |
| 6:5 | 00 | Reserved |
|  | 01 | Reserved |
|  | 10 | Reset Special Mask |
|  | 11 | Set Special Mask |
| 4 | Must be set to 0 |
| 3 | Must be set to 1 |
| 2 | 1 | Poll Command |
|  | 0 | No Poll Command |
| 1:0 | 00 | Reserved |
|  | 01 | Reserved |
|  | 10 | Next Read Returns Interrupt Request Register |
|  | 11 | Next Read Returns In-Service Register |